## Slide 1
PHYSICS · DIRECT CURRENT
Ohm's Law for
Closed Circuits
How a real source shares its voltage between the load and itself
R
r
+
−
I
external load
source interior
E = I(R + r)
A compact English teaching edition based on the original lesson

## Slide 2
THE HIDDEN RESISTOR
02
Battery heating reveals resistance inside the source.
A real battery is not an ideal voltage source.
When current flows, the battery warms because charges also lose energy inside the source.
Internal heat = I^2 r t
r is the internal resistance of the source.
The load resistance R is outside the source.

## Slide 3
ENERGY PER CHARGE
03
EMF measures how strongly a source can supply energy.
It is a property of the source, not a measure of stored charge.
E = W / q
1 volt = 1 joule per coulomb
chemical,
mechanical,
or light energy
electrical
energy
Non-electrostatic forces move charge from lower to higher electric potential inside the source.

## Slide 4
TWO DIFFERENT IDEAS
04
EMF supplies energy; terminal voltage delivers what remains.
Both use volts, but they describe different energy transfers.
INSIDE THE SOURCE
EMF E
energy added per coulomb by non-electrostatic forces
ACROSS THE TERMINALS
Terminal voltage U
energy delivered per coulomb to the external circuit
U = E − Ir

## Slide 5
ONE ENERGY BALANCE
05
Each coulomb receives E, then spends it across R and r.
The full-circuit equation follows directly from energy conservation.
SOURCE
energy supplied
E q
EXTERNAL LOAD
useful energy
I R q
+
SOURCE INTERIOR
internal heating
I r q
E q = I R q + I r q → E = I(R + r)

## Slide 6
THE CORE MODEL
06
Current is limited by both the load and the source.
Treat a real source as an ideal EMF E in series with internal resistance r.
R
r
+
−
I
external load
source interior
I = E / (R + r)
Increasing R reduces the current.
Increasing r also reduces the current.
If R → 0, the short-circuit current approaches E/r.

## Slide 7
VOLTAGE SHARING
07
The terminal voltage drops when the source supplies more current.
Part of the EMF is lost across the internal resistance.
E
Ir
internal voltage drop
U = E − Ir
voltage available to the load
Open circuit: I = 0, so U = E. Heavy load: I is large, so U is smaller.

## Slide 8
READ THE SOURCE FROM A GRAPH
08
A U-I graph reveals both EMF and internal resistance.
For a source, U = E − Ir is a straight line.
U
I
vertical intercept = E
horizontal intercept = E/r
SLOPE
ΔU / ΔI = −r

## Slide 9
WHERE THE POWER GOES
09
Internal resistance converts part of the source power into heat.
Efficiency improves when the load resistance is large compared with r.
source power
Psource = E I
=
I^2 R
+
I^2 r
USEFUL OUTPUT
Pload = I^2 R
EFFICIENCY
η = R / (R + r)

## Slide 10
WORKED EXAMPLE
10
One model answers current, voltage, and heating questions.
Given E = 3.0 V, R = 2.0 Ω, and r = 1.0 Ω.
2 Ω
1 Ω
+
−
I
1
Current
I = E/(R+r) = 3.0/3.0 = 1.0 A
2
Terminal voltage
U = IR = 1.0 × 2.0 = 2.0 V
3
Internal heating
Pinternal = I^2r = 1.0 W

## Slide 11
MEASURE E AND r
11
Two operating points are enough to determine the source.
Measure terminal voltage and current for two different loads.
R
r
+
−
I
Change R, then record (I, U).
Measurement 1
U1 = E − I1 r
Measurement 2
U2 = E − I2 r
r = (U1 − U2) / (I2 − I1)

## Slide 12
ORIGINAL PROBLEM · REWRITTEN
12
Use open-circuit voltage and loaded current to identify the source.
An ideal voltmeter and ammeter are connected as shown.
Data
Switch closed: U = 1.6 V, I = 0.4 A
Switch open: U = 2.0 V
Solution
E = 2.0 V
r = (E − U)/I = (2.0 − 1.6)/0.4 = 1.0 Ω

## Slide 13
APPLICATION
13
A motor receives less voltage when internal loss is significant.
The original lamp-and-motor circuit becomes an energy-accounting problem.
Reasoning path
Use the lamp rating to find the circuit current.
Apply E = I(R_total + r) in each switch position.
Motor input: Pin = Umotor I.
Motor output = input − coil heating.

## Slide 14
CONCEPT CHECK
14
Which statement about EMF is correct?
Choose one answer, then justify it using energy per charge.
A. EMF is simply the terminal voltage.
B. A larger EMF means the source must store more energy.
C. A larger EMF means the source must do work faster.
D. EMF equals the energy supplied by the source per unit charge.
Answer: D

## Slide 15
THE COMPLETE PICTURE
15
A real source supplies energy and consumes some of it.
Model the source, conserve energy, then interpret the result.
MODEL
ideal EMF E
+ internal resistance r
CURRENT
I = E / (R + r)
TERMINAL VOLTAGE
U = E − Ir = IR
EFFICIENCY
η = R / (R + r)
The central question is always: where does each joule per coulomb go?